## Slide 1
BOOLEAN FUNCTIONS Havirneanu Albert-Andrei
Notes: <number>

## Slide 2
Quine-Mc’Clusky’s Simplification method
The boolean function f is given in its Disjunctive Canonical Form.
Step 1: We order the support set of f, Sf = { (x1, x2, … , xn) | f(x1, x2, …, xn) = 1 }, in ascending/descending order, with respect to the number of ‘1’ values.
Step 2: We create a tableau, with each minterm on a line(minterms are represented using the power of variables from the function’s expression). They are arranged in asc/desc order with respect to the number of values ‘1’.
Step 3: We make groups of minterm, such that all the minterms belonging to the same group gave the same number of values ‘1’ as power of variables.
Only two neighbor groups can contain 2 adjacent monoms.

## Slide 3
Step 4: The result of the factorization of 2 neighbor monoms is a new monom represented as a row at the end of the tableau. The row contains the same values(0, 1, -) in the columns corresponding to the common variables and the symbol ‘-’ for the variable which is eliminated. All the new monoms obtained will form a new group(used further in higher order factorization).
The symbol ‘-’ cannot be combined with anything else.
The set of maximal monoms contains the monoms corresponding to all the unmarked rows from the tableau.
Step 5: For obtaining the central monoms we use a new tableau representing the correspondence between the maximal monoms(on columns) and the minterms from the function expression(on rows).
Step 6: A cell is marked with ‘*’ if the minterm corresponding to the row was used in factorization to obtain the maximal monom from the column. A maximal monom is a central monom if there is a ‘*’ on its column, which is unique on its row. The disjunction of all central monoms belongs to all simplified forms of the initial function.

## Slide 4
Step 7: According to the previous tableau, the minterms from the function’s expression which are uncovered by the central monoms will be covered in all possible ways using a minimum number of overlaps, resulting all simplified forms of the initial function.

## Slide 5
Exercise 5.8
Using Quine’s method, simplify the following Boolean function given by their values 0:
f8(0,0,1) = f8(1,0,1) = f2(1,1,0) = 0
f8(0,0,0) = f8(0,1,0) = f8(1,0,0) = f8(0,1,1) = f8(1,1,1) = 1
The Disjunctive Canonical Form is :
f2(x1,x2,x3) = m0 V m2 V m3 V m4 V m7
Ascending order => Sf = {(0,0,0), (0,1,0), (1,0,0), (0,1,1), (1,1,1)}

## Slide 6
Group | X1 X2 X3 | 
1 | 0 0 0 | m0
2 | 0 1 0 | m2
 | 1 0 0 | m4
3 | 0 1 1 | m3
4 | 1 1 1 | m7
5 = 1 + 2 | 0 - 0 | m0 V m2 = not(x1)not(x2)=max1
 | - 0 0 | m0 V m4 = not(x2)not(x3)=max2
6 = 2 + 3 | 0 1 - | m2 V m3 = not(x1)x2=max3
7 = 3 + 4 | - 1 1 | m3 V m7 = x2x3=max4

## Slide 7
Max monoms Minterms | max1 | max2 | max3 | max4
m0 | * | * |  | 
m2 | * |  | * | 
m3 |  |  | * | *
m4 |  | * |  | 
m7 |  |  |  | *

## Slide 8
M(f) = {max1 , max2 , max3 , max4}
C(f) = {max2 , max4}
M(f) ≠ C(f) and C(f) ≠ 0 => second case of simplification
g(x1 , x2 , x3) = max2 V max4 = not(x2)not(x3) V x2x3
There are 2 options(max3 or max1) for h(x1 , x2 , x3) => there are 2 simplified forms for f
f1(x1 , x2 , x3) = not(x2)not(x3) V x2x3 V not(x1)not(x2)
f2(x1 , x2 , x3) = not(x2)not(x3) V x2x3 V not(x1)x2